## Slide 1: Modeling Communication Systems Using the SystemC AMS Building Block Library
Jiong Ou1, Farooq Muhammad1, Christoph Grimm1 and Martin Barnasconi2
Vienna University of Technology1
NXP Semiconductors2

## Slide 2: Outline
A brief introduction to the SystemC AMS extensions
Overview of the AMS Building Block Library
Application example: Modeling of OFDM Transceiver System
Conclusions and Future work

## Slide 3: SystemC AMS extensions
SystemC AMS is not SPICE
SystemC AMS is not for circuit design – it‘s for overall system modeling!
Used in appropriate way, SystemC AMS yields
  high simulation performance
  increased design productivity

## Slide 4: SystemC AMS extensions
Specification
SystemC
SoC
Interface
AMS
D
RF
SystemVerilog, VHDL, Verilog
VHDL-AMS, Verilog-AMS
Functional
Architecture
Implementation
SystemC AMS extensions
NEW

## Slide 5: AMS Building Block Library - Motivation
Problems:
  Slow simulation of AMS communication systems
  Modeling of different parts of a system needs a serious investment in time
  Limitations and constraints of closed (proprietary) models not always clear
Possible Solutions:
  Modeling in Timed Data Flow (TDF)
  Provides building blocks for various AMS, RF, and digital functions
  Using open model-based design approach

## Slide 6: Available modules
Signal sources:
  Sine/Cosine, bit stream (uniformly), random number (gaussian) …
Signal processing:
  Basic mathematic modules: adder, multiplier, integrator …
  Analog modules: LNA, mixer, PLL, Butterworth/Chebyschev filter …
  Modulation processes: AM, BASK, M-FSK, M-PSK, DBPSK, OQPSK, QAM, OFDM …
  DSP algorithm: FFT/IFFT …
  Converter: A/D converter, D/A converter, P2S, S2P…
Analysis tools: eye diagram, scatterplot …

## Slide 7: Non-ideal properties of analog
LNA:
  intermodulation products (IP3)
  output limitation
General modules of non-idealities:
Mixer:
  intermodulation products (IP3)
  output limitation
AD/DA converter :
  gain error
  offset error
  output limitation
Saturation
Dead zone
Columb funciton

## Slide 8: Paramerterization of modules
Generally: Adaptivity of modules is realized by parametrization of modules; realization could be DSP SW, FPGA, maybe analog
  setting parameters by instantiation
  parameter adjustments during simulation possible for some modules
Name value | Type | Default value | Description
n | sc_module_name | - | name of instant module
_gain | double | - | gain in dB
_ip3 | double | - | IP3 in dBm
_ideal | bool | - | true for simulation of ideal LNA, otherwise false

## Slide 9: User-specific model extensions
The open nature of the AMS building block library enables making model extensions
  without changing the design architecture or structure!
Example: Add non-ideal effects to the model (e.g., noise)
9
Model-based design with Matlab/Simulink®
Open model-based design approach
+
Noise
+noise
void processing() {
out.write(ltf(…)+noise());
}
Jiong Ou, Farooq Muhammad, Christoph Grimm and Martin Barnasconi
Notes: MB: proposal for a new slide copied from Christoph – tuned the text for this presentation – please check with Christoph if he agrees!

## Slide 10: Building block example: LNA header file
SCA_TDF_MODULE (lna)
{
public:
sca_tdf::sca_in<double> in; // Input port
sca_tdf::sca_out<double> out; // Output port
private:
double gain; // Gain in dB
double ip3; // Third Input Intercept Point in dBm
// Coefficients of output polynomial v = a*i - b*i*i - c*i*i*i
double a, b, c;
bool ideal; // ideal lna or not, true --> ideal
...
public:
// Constructor: name, gain in dB, ip3 in dBm, ideal (bool)
lna (sc_core::sc_module_name n, double _gain, double _ip3, bool _ideal);
...
private:
void processing(); // Timed Data Flow (TDF) processing method
};
10
Jiong Ou, Farooq Muhammad, Christoph Grimm and Martin Barnasconi
LNA
in
out

## Slide 11: Example: OFDM Tranceiver(1)
OFDM: Orthogonal frequency-division multiplexing
OFDM
Transmitter
OFDM
Receiver
air
Notes: A large number of closely-spaced orthogonal sub-carriers are used to carry data,

## Slide 12: Example: OFDM Tranceiver(2)
Structure of the application:
air channel

## Slide 13: Example: OFDM Tranceiver(2)
/*** instantiate stimuli generator ***/
rand_bool i_stimuli("stimuli",16);
i_stimuli.out(sig_stimuli);
i_stimuli.out.set_timestep(1/freq_bit,SC_SEC);
/*** instantiate OFDM transmitter ***/
ofdm_se<8> i_tran("transmitter",freq_carrier,constl_dim,freq_bit,data_rate,ampl_se);
i_tran.in(sig_stimuli);
i_tran.out(sig_out);
/*** instantiate channel module ***/
air i_air("air",attent,"gauss_white",n_va);
i_air.in(sig_out);
i_air.out(sig_noise);
/*** instantiate OFDM receiver ***/
ofdm_re<8> i_receiver("receiver",freq_carrier,constl_dim,freq_bit,data_rate,ampl_re);
i_receiver.in(sig_noise);
i_receiver.out(sig_received);
/*** instantiate signal drain ***/
drain drn("drn");
drn.in(sig_received);

## Slide 14: Simulation results(1)
Parameters for simulation: (no noise, no attenuation)
constl_dim = 16, n_va = 0.0, ampl_se = 1.0, ampl_re = 1.0, atten = 0.0
Parameters for simulation: (with strong white noise, no attenuation)
constl_dim = 16, n_va = 90.0, ampl_se = 1.0, ampl_re = 1.0, atten = 0.0

## Slide 15: Simulation results(2)
Parameters for simulation: (with strong white noise and 50% attenuation)
constl_dim = 16, n_va = 90.0, ampl_se = 20.0, ampl_re = 0.1, atten = 0.5
With higher transmission power, we can reproduce the correct signals again!
Parameters for simulation: (with strong gaussian noise and 50% attenuation)
constl_dim = 16, n_va = 90.0, ampl_se = 1.0, ampl_re = 1.0, atten = 0.5

## Slide 16: Simulation results(3)
Parameters for simulation: (with strong gaussian noise and 50% attenuation)
constl_dim = 4, n_va = 90.0, ampl_se = 1.0, ampl_re = 1.0, atten = 0.5
Or we can also slow down the transmission to improve the Bit Error Rate (BER).

## Slide 17: Conclusions and Future work
It is convenient to model communication systems using the AMS building block library
  Open Source building block library is published and can be downloaded from http://www.systemc-ams.org/
  Already used by several companies for research purpose
Extend the Library with technology dependent information
  Evaluation of area and power consumption
  Enabling architecture exploration use cases